## Slide 1
全新五十鈴環保6型 38噸拖頭 | 
型號 Model | EXR52EZ-7S-VI-C
廢氣排放標準 Emission Standard | 環保六型 Euro VI
總拖量(公斤) G.C.W. (kg) | 38,000
乘客量 (連司機) Seating Capacity | 1 + 2 座位
車身尺吋 Dimensions | 
全長 (毫米) Overall Length (mm) | 5,790
全闊 (毫米) Overall Width (mm) | 2,490
全高 (毫米) Overall Height (mm) | 3,050
輪距 (毫米) Wheelbase (mm) | 3,450
引擎 Engine | 
型號 Model | 6WG1E6N
類別 Type | 直列式六氣缸，24氣閥，可變活瓣渦輪增壓 (VGS Turbo)連中置冷卻器， 廢氣再循環裝置 (EGR)，電子控制高壓共軌噴注系統 (CRS) 柴油微粒過濾器+選擇性催化還原 (DPD+SCR) In-line, 6 Cylinders, 24 Valves, Variable Geometry System Turbocharger (VGS Turbo) with Intercooler Exhaust Gas Recirculation (EGR), Common Rail System (CRS), Diesel Particulate Diffuser (DPD) + Selective Catalytic Reduction (SCR)
汽缸容積 (毫升) Displacement (cc) | 15,681
最大馬力 (匹/轉) Max. Output (PS/rpm) | 420 / 1,800
最大扭力 (公斤-米/轉) Max. Torque (kgm/rpm) | 190 / 1,300
油缸容積 (公升) Fuel Tank Capacity (litre) | 400
尿素缸容積 (公升) Adblue Tank Capacity (litre) | 28
波箱 Transmission | 
型號 Model | MJT7S 7前1後 手動波箱 7 Forward 1 Reverse, Manual
波段比 Gear Ratios | 1 ~ 7波：6.833 ~ 0.728
最終傳動比 Final Gear Ratio | 4.333
離合器 Clutch | 
類別 Type | 雙乾板式附避震彈簧，空氣輔助液壓控制 Dry Twin Plate with Cushioning Spring, Hydraulic Control with Air Assisted
轉向系統 Steering | 
類型 Type | 走珠式動力輔助轉向系統 Recirculating Ball with Power Assisted
懸掛系統 Suspension | 
前懸掛 Front | 龍船葉片式彈簧，雙重液壓吸震筒 Taper Leaf Spring, Double Acting Telescopic Shock Absorber
後懸掛 Rear | 半橢圓鋼合金多層葉片式彈簧 Semi-elliptical, Alloy Steel Leaf Spring
前軸 Front Axle | 倒置愛里奧工字架 Reverse Elliot "I" Beam
廠方設計負重 (公斤) Design Axle Loading (kg) | 7,500
運輸署批核負重 (公斤) Allocated Weight (kg) | 7,100
後軸 Rear Axle | 琵琶全浮內擺線齒輪 Banjo, Full Floating Type, Hypoid Gear
廠方設計負重 (公斤) Design Axle Loading (kg) | 13,000
運輸署批核負重 (公斤) Allocated Weight (kg) | 10,000
制動系統 Brake | 
制動操作 Service | 前後鼓剎，全風雙管路楔式制動，虛位自動調節器，電子制動系統 Front&Rear Drum, Full Air, Dual Circuit, Wedge Type, Brake Auto Adjuster, Electronic Brake System (EBS)
停車手制 Parking | 前後輪彈簧制動器 Spring Brake Actuators Acting on Front&Rear Wheels
輔助制動 Auxiliary | 廢氣剎車 Exhaust Brake
磨盤 Coupling | 
型號 Model | JOST JSK37C
設計負重 (公斤) Design Loading (kg) | 20,000
輪胎及車輪 Tire&Wheel | 
車胎 Tire | 295/80R22.5 無內膽原子胎 295/80R22.5 Tubeless Radial Tire
車輪 Wheel | 22.5 x 8.25 (10 螺絲) 22.5 x 8.25 (10 Studs)
標準裝備 Standard Equipment | 
 | 原廠冷氣，電腦錶板多功能顯示器(MID) AM/FM收音連CD機，駕駛席SRS安全氣囊 電動揭屋仔，氣墊避震駕駛室，氣墊座椅(駕駛座) 電動車窗，車門轉向輔助燈，中央門鎖 電動摺鏡臂(乘客座)，發熱線倒後鏡 Factory Built Air Conditioner, Multi-Information Display (MID) AM/FM CD Player, SRS Airbag on Driver Side Electrical Driven Tilt Cab, Cushioning Cab,Air Suspension Driver's Seat, Power Windows, Door Mount Cornering Lamps, Central Door Lock Electronic Retractable Side Mirror (Passenger Side), Heated Side Mirrors